## Slide 1
By
Dr. Srividya R
Associate Professor, Dept of ISE
BIOLOGY FOR COMPUTER ENGINEERS- BBOC407
Module -3
HUMAN ORGAN SYSTEMS AND BIO DESIGNS

## Slide 2: OVERVIEW
BRAIN as a CPU
EYE as a CAMERA System
HEART as a PUMP System
LUNGS as a PURIFICATION System
KIDNEY as a FILTERATION System

## Slide 3: Human Organ Systems and Bio designs
Brain as a CPU system (architecture, CNS and Peripheral Nervous System, signal transmission, EEG, Robotic arms for prosthetics. Engineering solutions for Parkinson’s disease).
Eye as a Camera system (architecture of rod and cone cells, optical corrections, cataract, lens materials, bionic eye).
Heart as a pump system (architecture, electrical signaling - ECG monitoring and heart related issues, reasons for blockages of blood vessels, design of stents, pace makers, defibrillators).
Lungs as purification system (architecture, gas exchange mechanisms, spirometry, abnormal lung physiology - COPD, Ventilators, Heart-lung machine).
Kidney as a filtration system (architecture, mechanism of filtration, CKD, dialysis systems).

## Slide 4
Human Organ Systems
The human body is a biological machine made up of various organ systems.
Organ systems are made up of various organs working together to perform a vital body function.
There are primarily 11 organ systems namely:
Skeletal system,
Muscular system,
Cardiovascular system,
Respiratory system,
Nervous system,
Digestive system,
Urinary system,
Endocrine system,
Lymphatic system,
Reproductive system,
Integumentary (Exocrine) system.

## Slide 5
Role and Function of Organ Systems
Biodesign is the use of living organisms in design.
Its processes can be used in the creation of fashion, textiles, furniture and architecture.
This presents a new frontier in terms of design with nature as opposed to design by nature in the case of bio-inspired design.
Bio-design was coined by William Myers in 2012 as:
“an emerging and often radical approach to design that draws on biological tenets and even incorporates the use of living materials into structures, objects and tools”

## Slide 6
Both CPU and brain use electrical signals to send messages.
The brain uses chemicals to transmit information; the computer uses electricity.
Even though electrical signals travel at high speeds in the nervous system, they travel even faster through the wires in a computer.
Both transmit information.
BRAIN AS A CPU SYSTEM

## Slide 9
CPU is the brain of a computer, containing all the circuitry needed to process input, store data, and output the results.
CPU is constantly following instructions of computer programs that inform as to which data needs to be processed and how.
The memory capacity of a human brain was testified to be equal to 2.5 petabytes, which is equivalent to 2.5 million gigabytes of memory.
Comparing computer and brain frequencies, Bostrom noted that:
“biological neurons operate at a peak speed of about 200 Hz, a full seven orders of magnitude slower than a modern microprocessor (∼2 GHz)”.
BRAIN AS A CPU SYSTEM

## Slide 10
The human brain is 1 part of the nervous system.
That’s the control system that sends instructions to all the other parts of body.
The human Brain has many different parts. Each one plays a different function.
But they all work together to manage complex thoughts, feelings and behaviours.
The 3 main parts of the brain
Fig: Parts of a neuron
Architecture of Human Brain

## Slide 11
On average, an adult human brain weighs about 1300 grams.
It uses about 20% of the body’s energy.
The brain helps coordinate all of the body’s internal and external actions.
Without your brain, you wouldn’t be able to sneeze, kick a ball or send a text.
Human Brain

## Slide 12
The brain has 3 main parts. They are the cerebrum, the cerebellum and the brainstem.
The cerebellum helps fine-tune your muscle movement. For example, it helps control balance, posture and motor learning.
The cerebrum is the largest part of the brain, spanning both the left and right hemispheres. --- It sits on top of the cerebellum and the brainstem. -- Many of the body’s higher functions rely on the cerebrum. -- For instance, it controls touch, vision, hearing, speech and fine motor skills, it interprets emotions, solve problems and learn.

## Slide 13
3. The brainstem connects base of the brain to the spinal cord.
-- It helps coordinate :
the brain’s communication with the rest of the body.
involuntary actions like breathing and heart rate.
Interior parts of the brain including:
(1) corpus callosum,
(2) thalamus,
(3) hypothalamus,
(4) pituitary gland, and
(5) pineal gland.

## Slide 14
Nervous System
The nervous system helps all parts of the body to communicate with each other.
It also reacts to changes both outside and inside the body.
The nervous system uses both electrical and chemical means to send and receive messages.
The nervous system has 2 main parts:
1. The central nervous system (CNS)
2. The peripheral nervous system (PNS)

## Slide 15
1. The central nervous system (CNS) :
CNS is made up of the brain and spinal cord.
Brain is the body’s “control center”
The CNS has various centers located within it that carry out the sensory, motor and integration of data.
These centers can be subdivided to Lower Centers (including the spinal cord and brain stem) and higher centers communicating with the brain via effectors.
CNS is usually considered to have 7 basic parts: the spinal cord, the medulla, the pons, the cerebellum, the midbrain, the diencephalon, and the cerebral hemispheres.
2. The peripheral nervous system (PNS) :
It is made up of nerves that branch off from the spinal cord and extend to all parts of the body.

## Slide 17
SIGNAL TRANSMISSION
A neuron (i.e., presynaptic ) sending a signal releases a chemical called a neurotransmitter.
Neurotransmitter binds to a receptor on the surface of the receiving neuron (i.e., postsynaptic).
ELECTRO ENCEPHALO GRAM [EEG]
It’s a test that measures electrical activity in the brain using small, metal discs (electrodes) attached to the scalp.
Brain cells communicate via electrical impulses and are active all the time, even during asleep.
This activity shows up as wavy lines on an EEG recording.
An EEG is one of the main diagnostic tests for epilepsy.

## Slide 18
ELECTRO ENCEPHALO GRAM [EEG]
An EEG can also find changes in brain activity that might be useful in diagnosing brain disorders.
An EEG might also be helpful for diagnosing or treating:
Brain tumors
Brain damage due to head injury
Brain dysfunction that can have a variety of causes (encephalopathy)
Sleep disorders
Inflammation of the brain (herpes encephalitis)
Stroke
Creutzfeldt-Jakob disease etc.

## Slide 19
ROBOTIC ARMS FOR PROSTHETICS
Robotic prosthetic limb is a well-established research area.
It integrates:
advanced mechatronics,
intelligent sensing, and control
It achieves higher order lost sensorimotor functions.
It maintains the physical appearance of amputated limb.
Robotic prosthetic limbs are expected to:
Replace the missing limbs of an amputee.
Restore the lost functions and providing aesthetic appearance.

## Slide 20
With the advancement of sensor technology, in the last few decades significant contributions have been made in this area.
The main aspects are:
enhanced social interaction
comfortable amputee’s life and
productive amputee to the society.
Deep Brain Stimulation(DBS)
DBS involves:
surgically implanting a neurotransmitter that sends electrical impulses to specific areas of brain
This procedure has helped people with Parkinson's reduce symptoms such as:
tremor
rigidity and
bradykinesia.

## Slide 21
The human eye is a wonderful instrument, relying on refraction and lenses to form images.
There are many similarities between the human eye and a camera, including:
A diaphragm to control the amount of light that gets through to the lens. This is the shutter in a camera, and
The pupil, at the center of the iris, in the human eye, is a lens to focus the light and create an image.
The image is real and inverted. A method of sensing the image.
In a camera, film is used to record the image; in the eye, the image is focused on the retina, and a system of rods and cones is the front end of an image-processing system that converts the image to electrical impulses and sends the information along the optic nerve to the brain.
EYE AS A CAMERA SYSTEM

## Slide 22
Photoreceptors in the retina are classified into two groups, named after their physical morphologies, into rods and cones. These photoreceptors are localized around an area near the centre of the retina called the macula, which is the functional center of the retina
OPTICAL CORRECTIONS
A slight modification of geometrically correct lines (as of a building) for the purpose of making them appear correct to the eye. The ability to see images or objects with clear, sharp vision results from light entering the eye. Light rays bend or refract when they hit the retina, sending nerve signals to the optic nerve, which then sends these signals to the brain. The brain processes them into images, allowing you to understand what you see

## Slide 23
CATARACT
A cataract is a clouding of the normally clear lens of the eye. At first, the cloudiness in your vision caused by a cataract may affect only a small part of the eye's lens and you may be unaware of any vision loss. As the cataract grows larger, it clouds more of your lens and distorts the light passing through the lens. This may lead to more-noticeable symptoms. A cataract is a cloudy lens. The lens is positioned behind the colored part of your eye (iris). The lens focuses light that passes into your eye, producing clear, sharp images on the retina — the light-sensitive membrane in the eye that functions like the film in a camera.
As you age, the lenses in your eyes become less flexible, less transparent and thicker. Age-related and other medical conditions cause proteins and fibers within the lenses to break down and clump together, clouding the lenses

## Slide 24
EYE LENS MATERIALS
Corrective spherocylindrical lenses are commonly used to treat refractive errors such as myopia, hyperopia, presbyopia, and astigmatism.
Both lenses and prisms are also frequently used to improve eye alignment and treat diplopia in strabismus.
Eyeglasses also serve an important role in protecting the eyes from physical trauma and harmful radiation.
Lenses can be produced using a variety of materials and designed with several optical profiles to optimize use in specific applications.
There are 4 main types of lens materials for eyeglasses and sunglasses. Each type of lens material can help correct refractive errors such as nearsightedness, farsightedness, astigmatism, or presbyopia

## Slide 25
Types of lens materials:
CR-39 -The most commonly used plastic lens material
Crown Glass is the most commonly used clear glass for ophthalmic lenses. In general, glass is the most durable material used for lenses. Crown glass is used mainly for single vision lenses and the distance carrier for most glass bifocals and trifocals.
Flint Glass uses lead oxides in its chemical make up to increase its index of refraction to approximately 1.58 to 1.69. Its Abbe value ranges from 30 to 40. This material is relatively soft, displays a brilliant luster and has chromatic aberration.
4. Polycarbonate Lenses
Polycarbonate lenses were first developed by a company named Gentex. Polycarbonate is a thermoplastic which means it is moldable under sufficient heat.

## Slide 26
BIONIC EYES
Bionic eye, is an electrical prosthesis which is surgically implanted into a human eye in order to allow for the transduction of light (the change of light from the environment into impulses the brain can process) in people who have sustained severe damage to the retina.
The bionic eye comprises an external camera and transmitter and an internal microchip.
The camera is mounted on a pair of eyeglasses, where it serves to organize the visual stimuli of the environment before emitting high-frequency radio waves
https://www.youtube.com/watch?v=05ee61Bu-Ok&t=1s
www.youtube.com/watch?v=WhYe6REdljw

## Slide 28
HEART AS A PUMP SYSTEM
Heart is sort of like a pump, or two pumps in one. The right side of your heart receives blood from the body and pumps it to the lungs.
The left side of the heart does the exact opposite: It receives blood from the lungs and pumps it out to the body.
The human heart is very strong and is capable of pumping blood up to 30 feet distance.
An average heart beats maximum of 70-80 beats per minute and is considered healthy.
The efficiency of the heart can be maintained and improved by performing physical activity.

## Slide 29
Heart - Pump Of The Circulatory System
Do you know that in a year your heart beats over 30 million times?
This means in a lifespan of 80 years, it would be around 2.5 billion times.
How does the heart make up its pace?
What are the different parts of a heart?

## Slide 31
ELECTRICAL SIGNALING
The sinus node generates an electrical stimulus regularly, 60 to 100 times per minute under normal conditions. The atria are then activated. The electrical stimulus travels down through the conduction pathways and causes the heart's ventricles to contract and pump out blood.
ECG MONITORING
ECG monitoring systems have been developed and widely used in the healthcare sector for the past few decades and have significantly evolved over time due to the emergence of smart enabling technologies.
Nowadays, ECG monitoring systems are used in hospitals, homes, outpatient ambulatory settings, and in remote contexts.
They also employ a wide range of technologies such as IoT , edge computing, and mobile computing.
In addition, they implement various computational settings in terms of processing frequencies, as well as monitoring schemes.
They have also evolved to serve purposes and targets other than disease diagnosis and control, including daily activities, sports, and even mode-related purposes.
https://www.youtube.com/watch?v=kwLbSx9BNbU

## Slide 33
Cardiovascular diseases including heart failure (HF).
REASONS FOR BLOCKAGES OF BLOOD VESSELS: Coronary artery disease is a common heart condition. The major blood vessels that supply the heart (coronary arteries) struggle to send enough blood, oxygen and nutrients to the heart muscle. Cholesterol deposits (plaques) in the heart arteries and inflammation are usually the cause of coronary artery disease. Signs and symptoms of coronary artery disease occur when the heart doesn't get enough oxygen-rich blood.

## Slide 37
DESIGN OF STENTS
A stent is a tiny tube that can play a big role in treating your heart disease. It helps keep your arteries -- the blood vessels that carry blood from your heart to other parts of your body, including the heart muscle itself -- open.
Why Would You Need a Stent?
If a fatty substance called plaque builds up inside an artery, it can reduce blood flow to your heart. This is called coronary heart disease and it can cause chest pain.
DESIGN
The majority of these stents are constructed from a nickel titanium alloy. Balloon expandable stents are susceptible to permanent deformation when they are compressed extrinsically, which is not an issue in the coronary tree.

## Slide 38
PACE MAKERS
A pacemaker is a small device that's placed (implanted) in the chest to help control the heartbeat.
It's used to prevent the heart from beating too slowly. Implanting a pacemaker in the chest requires a surgical procedure. A pacemaker is also called a cardiac pacing device.
Types
Single chamber pacemaker. This type usually carries electrical impulses to the right ventricle of your heart.
Dual chamber pacemaker. This type carries electrical impulses to the right ventricle and the right atrium of your heart to help control the timing of contractions between the two chambers.

## Slide 39
https://www.youtube.com/watch?v=WgKCUjPcDY0

## Slide 40
A pacemaker has two parts:
Pulse generator. This small metal container houses a battery and the electrical circuitry that controls the rate of electrical pulses sent to the heart.
Leads (electrodes). One to three flexible, insulated wires are each placed in one or more chambers of the heart and deliver electrical pulses to adjust the heart rate. However, some newer pacemakers don't require leads. These devices, called leadless pacemakers, are implanted directly into the heart muscle.

## Slide 41
DEFIBRILLATORS
Defibrillators are devices that send an electric pulse or shock to the heart to restore a normal heartbeat.
they are used to prevent or correct an arrhythmia, an uneven heartbeat that is too slow or too fast.
If the heart suddenly stops, defibrillators can also help it beat again. Different types of defibrillators work in different ways.
Automated external defibrillators (AEDs), which are now found in many public spaces, are used to save the lives of people experiencing cardiac arrest.
Even untrained bystanders can use these devices in an emergency.

## Slide 42
There are three types of defibrillators: AEDs, ICDs, and WCDs.
An AED is a lightweight, battery-operated, portable device that checks the heart’s rhythm and sends a shock to the heart to restore normal rhythm. The device is used to help people having cardiac arrest.
ICDs are placed through surgery in the chest or stomach area, where the device can check for arrhythmias. Arrhythmias can interrupt the flow of blood from your heart to the rest of your body or cause your heart to stop. The ICD sends a shock to restore a normal heart rhythm.
WCDs have sensors that attach to the skin. They are connected by wires to a unit that checks your heart’s rhythm and delivers shocks when needed. Like an ICD, the WCD can deliver low- and high-energy shocks. The device has a belt attached to a vest that is worn under your clothes.

## Slide 43: LUNGS AS A PURIFICATION SYSTEM
INTRODUCTION:
Every cell in your body needs oxygen to live. The air we breathe contains oxygen
and other gases. The respiratory system's main job is to move fresh air into your
body while removing waste gases.
Once in the lungs, oxygen is moved into the bloodstream and carried through your body.
At each cell in your body, oxygen is exchanged for a waste gas called carbon dioxide. Your bloodstream then carries this waste gas back to the lungs where it is removed from the bloodstream and then exhaled.

## Slide 44
Your lungs and the respiratory system automatically perform this vital process, called gas exchange.
In addition to gas exchange, your respiratory system performs other roles important to breathing. These include:
Bringing air to the proper body temperature and moisturizing it to the right humidity level.
Protecting your body from harmful substances. This is done by coughing, sneezing, filtering, or swallowing them.
Supporting your sense of smell.

## Slide 45: How the Lungs Work
The lungs are a vital part of the respiratory system, which allows you to breathe.
In addition to the lungs, the respiratory system includes airways that carry air in
and out of your lungs, blood vessels surrounding the lungs, and the muscles that
help you breathe.
Airways
The body uses several channels to bring oxygen-rich air into the lungs and release carbon dioxide (a waste gas) out of the lungs. The body’s airways include:
Nasal cavities
Mouth
Voice box (called the larynx)
Windpipe (called the trachea)
Bronchial tubes

## Slide 46
When you take a breath through your nose or mouth, the air is warmed and humidified, and then moved through your voice box and down the windpipe. From there, it travels down two bronchial tubes that enter the lungs.
A thin flap of tissue, the epiglottis, blocks your windpipe when you swallow to prevent food and liquid from entering.
When you breathe out, air leaves the body through your airways.

## Slide 48
ARCHITECTURE:
The primary function of the lungs is gas exchange. However, the lungs perform several
important non-respiratory functions that are vital for normal physiology.
The lung, with its unique ability to distend and recruit pulmonary vasculature, acts as a reservoir of blood, fine-tuning preload to the left heart to optimize cardiac output.
* The lung acts as a filter against endogenous and exogenous emboli, preventing them from
accessing systemic circulation.
Pulmonary epithelium forms the first line of defense against inhaled particles.
*
* Pulmonary endothelial cells are responsible for the uptake, metabolism, and
biotransformation of several exogenous and endogenous substances.
*
Pulmonary metabolic capacity is easily saturated, but pulmonary endothelial binding of
some drugs alters their pharmacokinetics.

## Slide 50: GAS EXCHANGE MECHANISMS:
Air enters the body through the mouth or nose and quickly moves to the pharynx or throat. From there, it
passes through the larynx, or voice box, and enters the trachea.
The trachea is a strong tube that contains rings of cartilage that prevent it from collapsing. Within the lungs, the trachea branches into a left and right bronchus. These further divide into smaller and smaller branches called bronchioles. The smallest bronchioles end in tiny air sacs. These are called alveoli.
They inflate when a person inhales and deflate when a person exhales. During
gas exchange oxygen moves from the lungs to the bloodstream.
At the same time, carbon dioxide passes from the blood to the lungs. This happens in the lungs between the alveoli and a network of tiny blood vessels called capillaries, which are located in the walls of the alveoli.

## Slide 52: Spirometry
Spirometry uses a machine called a spirometer. A spirometer is a medical device that consists of a mouthpiece and a tube.
They connect to a machine that measures your airflow.
It is the most common of the pulmonary function tests.
It measures lung function, specifically the amount and/or speed of air that can be inhaled and exhaled
And used to diagnose asthma, chronic obstructive pulmonary disease (COPD) and other conditions that affect breathing.

## Slide 54
Requirements of an acceptable spirometer
are:
Spirometers must be able to accumulate volume for ≥15 s.
The measuring volume should be ≥8 L (body
temperature and pressure, saturated).
The accuracy of reading should be at least ±3%
(or ±0.05 L) with flows from 0–14 L per s.
•
The total resistance to airflow at 14 L per s
should be <1.5 cmH2O per L per s (<0.15 kPa
per L per s).

## Slide 55
rib fractures: Fracturing a rib can lead to numerous lung complications such as pneumothorax, lung contusion, and even respiratory failure.using an incentive spirometer can help reduce these complications and help the lungs work better.
pneumonia: Incentive spirometry is commonly used to break up mucus buildup that builds up in the lungs in people with pneumonia.
chronic obstructive pulmonary disease (COPD). COPD is a group of respiratory disorders that are most commonly caused by smoking. There’s no current cure, but quitting smoking, using a spirometer, and following an exercise plan can help manage symptoms.
cystic fibrosis: People with cystic fibrosis might benefit from using an incentive spirometer to clear fluid buildup. A 2015 studyTrusted Source found that spirometry has the potential to reduce pressure in the chest cavity and lower the chance of central airway collapse.
other conditions: A doctor may also recommend an incentive spirometer for people with sickle cell anemia, asthma, multiple sclerosis, or atelectasis.

## Slide 56
Chronic obstructive pulmonary disease (COPD). COPD is a group of respiratory disorders that are most commonly caused by smoking. There’s no current cure, but quitting
smoking, using a spirometer, and following an exercise plan can help manage symptoms.

## Slide 57
COPD:
Chronic obstructive pulmonary disease (COPD)
is a chronic inflammatory lung
disease that causes obstructed airflow from the lungs.
Symptoms include breathing difficulty, cough, mucus (sputum) production, and wheezing.
It's typically caused by long-term exposure to irritating gases or particulate matter, most often from cigarette smoke. People with COPD are at increased risk of developing heart disease, lung cancer, and a variety of other conditions.
Emphysema and chronic bronchitis are the two most common conditions that contribute to COPD. These two conditions usually occur together and can vary in severity among individuals with COPD.
Symptoms
COPD symptoms often don't appear until significant lung damage has occurred, and they usually worsen over time, particularly if smoking exposure continues.

## Slide 58
Signs and symptoms of COPD may include:
Shortness of breath, especially during physical activities
Wheezing
Chest tightness
A chronic cough that may produce mucus (sputum) that may be clear, white, yellow, or greenish
Frequent respiratory infections
Lack of energy
Unintended weight loss (in later stages)
Swelling in ankles, feet, or legs
Tests may include:
Lung (pulmonary) function tests.
Chest X-ray.
CT scan.
Arterial blood gas analysis.
Laboratory tests.

## Slide 60: Ventilators
A ventilator is a device that supports or takes over the breathing process, pumping air into the lungs.
Types of ventilator
Face mask ventilators
Mechanical ventilators
Manual resuscitator bags
Tracheostomy ventilators

## Slide 61: Face mask ventilator
It is a noninvasive method of supporting the breathing and oxygen levels.
The mask fits over the nose and mouth while air blows into the airways and lungs.
Mechanical ventilator
These are machines that take over the breathing process entirely .
It work via a tube in a person’s throat, pumping air into the lungs and transporting carbon dioxide away.

## Slide 62: Manual Resuscitator Bags
These are pieces of equipment that allow person to control the airflow of their ventilator with their hands.
These devices consist of an empty bag or bladder that a person squeezes to pump air into the lungs.
Tracheostomy ventilator
A tracheostomy is a procedure where a doctor creates an opening in the windpipe and inserts a tube, which allows air to flow in and out. This enables a person to breathe without using their nose or mouth.

## Slide 63
KIDNEY AS FILTRATION SYSTEM INTRODUCTION:
Kidneys remove wastes and extra fluid from the body. Kidneys also remove acid that is produced by the cells of the body and maintain a healthy balance of water, salts, and minerals—such as sodium, calcium, phosphorus, and potassium—in the blood. Without this balance, nerves, muscles, and other tissues in the body may not work normally.
Kidneys also make hormones that help
Control blood pressure.
Make red blood cells NIH external link.
Keeps bones strong and healthy.

## Slide 64
ARCHITECTURE:
The kidneys are two bean-shaped organs, each about the size of a fist.
They are located just below the rib cage, one on each
side of the spine.
Healthy kidneys filter about a half cup of blood every minute, removing wastes and extra water to make urine.
The urine flows from the kidneys to the bladder through two thin tubes of muscle called ureters, one on each side of the bladder. Your bladder stores urine. Kidneys, ureters, and bladder are part of your urinary tract

## Slide 65
MECHANISM OF FILTRATION:
Each kidney is made up of about a million filtering units called nephrons. Each nephron
includes a filter, called the glomerulus, and a tubule.
The nephrons work through a two-step process: the glomerulus filters blood, and the tubule returns needed substances to your blood and removes wastes.
Each nephron has a glomerulus to filter your blood and a tubule that returns needed substances to your blood and pulls out additional wastes. Wastes and extra water become urine.
The glomerulus filters your blood
As blood flows into each nephron, it enters a cluster of tiny blood vessels—the glomerulus.
The thin walls of the glomerulus allow smaller molecules, wastes, and fluid—mostly water—to pass into the tubule. Larger molecules, such as proteins and blood cells, stay in the blood vessel. The tubule returns needed substances to your blood and removes wastes.

## Slide 66
How does blood flow through my kidneys?
Blood flows into the kidney through the renal artery. This large blood vessel branches into smaller and smaller blood vessels until the blood reaches the nephrons. In the nephron, blood is filtered by the tiny blood vessels of the glomeruli and then flows out of the kidney through the renal vein.
Blood circulates through your kidneys many times a day. In a single day, kidneys filter about 150 quarts of blood. Most of the water and other substances that filter through your glomeruli are returned to the blood by the tubules. Only 1 to 2 quarts become urine.
When the kidney doesn't function properly, Chronic kidney disease occurs when a disease or condition impairs kidney function, causing kidney damage to worsen over several months or years

## Slide 67
CKD:
Chronic kidney disease includes conditions that damage your kidneys and decrease their ability to keep you healthy by filtering wastes from your blood. If kidney disease worsens, wastes can build to high levels in your blood and make you feel sick. You may develop complications like
high blood pressure
anemia (low blood count)
weak bones
poor nutritional health
nerve damage
SYMPTOMS:
People with CKD may not feel ill or notice any symptoms. The only way to find out for sure if you have CKD is through specific blood and urine tests. These tests include the measurement of both the creatinine level in the blood and the protein in the urine.

## Slide 68
TREATMENT:
Depending on the cause, some types of kidney disease can be treated. Often, though, chronic kidney disease has no cure. Treatment usually consists of measures to help control signs and symptoms, reduce complications, and slow the progression of the disease. If your kidneys become severely damaged, you might need treatment for end- stage kidney disease.
DIALYSIS:
Dialysis is a procedure to remove waste products and excess fluid from the blood when the kidneys stop working properly. It often involves diverting blood to a machine to be cleaned.
There are 2 main types of dialysis:
Haemodialysis involves diverting blood into an external machine, where it's filtered before being returned to the body
Peritoneal dialysis involves pumping dialysis fluid into the space inside your abdomen (tummy) to draw out waste products from the blood passing through vessels lining the inside of the abdomen

## Slide 70
THANK YOU